## Slide 1: Updates on Research Data Management with hands-on session
Victor Dudarev, Markus Stricker, Alfred Ludwig

## Slide 2: Blocking Factors?
ECSA – ElectroChemical Surface Area (ElectroChemically active Surface Area)
SDC – Scanning Droplet Cell
SECCM – Scanning ElectroChemical Cell Microscopy
Standards in electrochemical measurements need to be established
(ECSA for SDC and long-range SECCM)
      If different measurement protocols have a severe impact on the target values of the metric / benchmark, what can you expect from trying to take all the data into account?
Missing process standards (next slides):
Sample storage
Annealing
Characterization chain

## Slide 3: Sample storage (oxidation?): Air exposure time workflow
https://crc1625.mdi.ruhr-uni-bochum.de/custom/editsample/0/
Sample
Treatment:
Air exposure
Sample_2
Air exposure time (in total): 0
Air exposure time (in total): 15
“Air-free” samples: Air exposure time must be specified for every sample state!
Characterisation: XPS, EDX, XRD, Resistance, Bandgap, …
characterisation of a sample that has not seen air
Characterisation: XPS, EDX, XRD, Resistance, Bandgap, …
characterisation of a sample that saw air
…
Next treatment:

## Slide 4: Missing process standards (annealing)
Sample
Treatment:
annealing,
oxidation,
polishing, …
Sample_2
Synthesis_2
Synthesis
https://crc1625.mdi.ruhr-uni-bochum.de/object/10701-agaupdpt-30-rpm-substrate-rotation-speed_2-27797
Let’s consider life example (SampleID 10701):
https://crc1625.mdi.ruhr-uni-bochum.de/object/10701-agaupdpt-30-rpm-substrate-rotation-speed_2-27797

## Slide 5: Missing process standards (characterization chain)
https://crc1625.mdi.ruhr-uni-bochum.de/rubric/area-a
https://crc1625.mdi.ruhr-uni-bochum.de/object/standard-screening-crc-aka-tobias-report-103066
Solution: set up the workflow by defining characterisation for the experiment (idea or plan)
and track the progress.
Idea or Plan
1) Create “plan” object
2) Define characterisations
3) Add samples and measurements…
4) Monitor workflows via reports in the “plan” object

## Slide 6: Types (Data formats)
What data can you read?
https://crc1625.mdi.ruhr-uni-bochum.de/adminobject
Types (Data formats)

## Slide 7: What is machine-readable data?
Research data management is not about just storing files, but about storing also metadata and probably data, extracted from the files and effective search afterwards. We need a programmatic ability to EXTRACT meaningful data/metadata from the file. A file format is in a "machine-readable" format for RDMS in either of two cases: 1) file format is standardised and well-described (from this description it should be obvious, how to get the required data, that researchers need => we can develop by ourselves); 2) The file format could be a proprietary one, but a program library/API exists that can extract required data (from the device manufacturer or some open-source packages).
There should be a clear understanding of what metadata (parameter names) should be extracted and stored in RDMS for effective search later.
Even having a machine-readable file is not enough, since it’s required to negotiate and standardise what would be meaningful parameters for the search / dataset generation regarding a particular data type.
Description for every type (measurement): what parameters, describing data/metadata are required to store and make it searchable!

## Slide 8: Extensible Data Support in RDMS
    To support a new kind of document/measurement, we create a new type in RDMS.
    Questions:
    How to validate data?
    How to extract metadata?
    How to extract data?
    Two approaches
    Manual Automated
    Write a Web-services for:
    Data validation on upload
    Data & metadata extraction
    Data visualization
    Everything is automated.
    Zero-code effort:
    No data validation on upload
    Templates to edit data/metadata
    Manual template guided data input, if required (file is considered raw, i.e. unprocessed)
    Continuous Development

## Slide 9: INF Meetings with projects
* SECCM Long-range: https://crc1625.mdi.ruhr-uni-bochum.de/object/10648-her-seccm-long-range-raw-27785
Thank you for your input!
First+ round:
A01 (except computational)
A02
A03
B01
B03
B04
B05
C02
C03
C04
S
Still not covered:
A01 (computational)
A04
B02
C01*
Team:
Prof. Markus Stricker (INF, A05)
Victor Dudarev (INF)
Doaa Mohamed (INF)
Behnam Mardani (A05)
Samuel García (A06)
Questions:
Research workflow
Expected Data Contributions (documents / properties)
Interaction with other projects data
Leverage Data Usage (FAIR)
  Imagine you have 10000+ documents:
  how would you structure them?
  what properties should be associated with every document (F - Findable)?
  what data you need to get from RDMS for your research (what format)?

## Slide 10: Supported Data Types & Formats
Supported data extraction: EDX, XRD Processed, BET Adsorption, Resistance, Thickness
PDF
TXT
CSV
Excel

## Slide 11: PDF Data Extraction: BET adsorption data
Goal: extract surface area from PDF measurement report
BET - Brunauer, Emmett & Teller (BET) equation Leon Müller, C02 (CRC 247)
https://crc247.mdi.ruhr-uni-bochum.de/object/ac008-ht_lmueller_report-n2-bet-25320
https://crc247.mdi.ruhr-uni-bochum.de/object/ac008-lacoo3-24922
Properties at the document level (BET adsorption report):
Properties at the sample level:
BET adsorption
Sample

## Slide 12: Data Extraction From File Name

## Slide 13: Parameters Extraction from File Name
File Name (Key1-Value1 Key2-Value2 … KeyN-ValueN):
Parsing of file name:
1) Split by " " (could be any other symbol);
=> collection of Key-Value pairs
2) Split by first "-" (could be any other symbol)
=> [ { key1, value1 }, … , { keyN, valueN } ]
Together with С03
SampleID-10598 AgAuCuPdPt LSV Date-250219 LSV_Cycle-10 Electrolyte-100mM-HClO4+900mM-NaClO4 ScanRate-0.005 EndPotential--0.858 ReferenceElectrode-MSE.csv
Composition: AgAuCuPdPt
Sample ID: 10598
Date: 2019-02-25
LSV_MA: 10
Electrolyte_Concentration: 100mM HClO4+900mM NaClO4
ScanRate: 0.005 (5mV/s)
EndPotential: -0,858 V
ReferenceElectrode: MSE

## Slide 14: Materials Library: Data Integration
https://inf.mdi.ruhr-uni-bochum.de/object/demo-ag-au-cu-pd-pt-ti-28840
Measurement Area
(composition)
Phases: [ Phase1,
…, PhaseN ]
Resistance: __ Ohm
Thickness: __ nm
Bandgap: __ eV
…
Sputtering & characterization:
Add Sample object (chemical system + substrate)
Add EDX CSV (or txt)
Add other characterization documents (repeat)
Get dataset on the sample page:
JSON
CSV

## Slide 15: Interlinking objects: A03 use case (Liang Yanyan)
Data by Liang Yanyan:
https://crc1625.mdi.ruhr-uni-bochum.de/rubric/a03
https://crc1625.mdi.ruhr-uni-bochum.de/report/usersstatistics
Summary:
Objects: 59
  Idea/experiment plan: 1
  Python Script (ipynb): 1
  Simulation Database (CSV): 57
Projects: 20
Links: 0

## Slide 16: Establishing properties/template: A03 use case (Liang Yanyan)
Data by Liang Yanyan:
https://crc1625.mdi.ruhr-uni-bochum.de/rubric/a03_agaupdpt_ag13_au45_pd24_pt18_surface-segregation-in-111-at-t300k
Properties to extract:
Temperature
Data Source
Inconsistent description (w.r.t. folder path specification)
List of the objects:
Template:

## Slide 17: Search: A03 use case (Liang Yanyan)
Data by Liang Yanyan:
https://crc1625.mdi.ruhr-uni-bochum.de/search/?typeid=94&createdbyuser=47&pr0name=Temperature&pr0type=Float&pr0min=300&pr0max=500&pr1name=SourcePath&pr1type=String&pr1max=3&pr1str=MDruns&prcnt=2
Use properties on search:
Temperature in [300; 500] and SourcePath contains 'MDruns' and type is Simulation Database (zip, db, csv) and user-creator is Liang Yanyan

## Slide 18: RDMS: Sort order in tables
https://crc1625.mdi.ruhr-uni-bochum.de/search/?system=Pt-Ru&typeid=6
Use case: get samples containing specific elements and order by arity of chemical system (N) and creation date
To sort in a complex way (by 2+ columns):
use "Shift" key while making the sort selection:

## Slide 19: RDMS: Advanced Interlink Objects
User view: https://demo.mdi.ruhr-uni-bochum.de/object/ag2s-4870
Admin view: https://demo.mdi.ruhr-uni-bochum.de/adminobject/edititem/4870
Example: establishing graph above objects
To add associated objects:
0) Go to “List edit” or select object to edit
1) Select associated object type (optional filter)
2) Input search phrase, contained in the Name of the desired object to be associated
3) Select (if required) link/association type object.
4) Drag & Drop desired object(s) from search result list to the area / adjust list
5) Save changes
directed graph
a
b
a
c
Important: Reverse associations allow to browse reverse- directional associations.

## Slide 20: Graph: always think about object connections
In Project: add unlinked objects. https://mdi.matinf.pro/rubric/industry
In Object (under associated objects): add linked objects.
https://mdi.matinf.pro/object/standard-screening-crc-aka-tobias-report-103066
Add “top level” objects
Add “children/dependent” objects
https://mdi.matinf.pro/rubric/industry
https://mdi.matinf.pro/object/standard-screening-crc-aka-tobias-report-103066

## Slide 21: Graph visualisation
https://mdi.matinf.pro/object/co-cu-mo-ni-equiatomic-library-117099
https://mdi.matinf.pro/object/graph/co-cu-mo-ni-equiatomic-library-117099
Motivation: understand relationship between objects
Interactive graph
JSON
JSON description

## Slide 22: A03 use case: adding missing objects and links
Initial object structure: Idea, Simulation database
Desired object structure: Idea -> System -> Composition -> Simulation database
Motivation: fill the gap between Idea and Simulation database
Types: System: Calculation/Computational Sample
Composition: Calculation/Computational Composition
https://crc1625.mdi.ruhr-uni-bochum.de/rubric/a03
https://crc1625.mdi.ruhr-uni-bochum.de/rubric/a03_ag-au-cu-pd-pt
Composition_1-1
System_1
System_N
Idea or Plan
Composition_1-K
Composition_N-1
Composition_N-L
Sim DBi
Sim DBi
Sim DBi
Sim DBi
Sim DBi
Sim DBi
Sim DBi
Sim DBi
…
Missing part

## Slide 23: Links to external resources Use Case: Slack

## Slide 24: Link to a Slack chat / action team
Goal: establish a link to a Slack discussion (channel/section/personal), related to the subject
Example: Creation of a “Request for Synthesis” object:
https://crc1625.mdi.ruhr-uni-bochum.de/adminobject/newitem/83?idr=226
https://crc1625.mdi.ruhr-uni-bochum.de/object/integrate-kg-and-rdms-25368
paste
Link to the Slack channel:
Use Case Generalisation: any String property with “*_Link” name behaves like a hyperlink.

## Slide 25: Context is a key!

## Slide 26: EDX Upload: Context matters!
https://mdi.matinf.pro/object/240409-k3-1-70357
Motivation: process raw EDX data (txt from machine)
Goal: exclude substrate/contamination artefacts from composition
Solution: context-aware data processing (get chemical system) (leave elements of interest only)
EDX
Sample
Context:
access to parent objects to get their data
Chemical System: Co-Fe-La-O-V
Context

## Slide 27: Context Matters: implications
Object
Parent_1
Context
Parent_N
…
Definition: context includes data on all parent objects and their data
Implication 1 (self-evident):
object linkage matters!
Implication 2:
document upload could result in different data outcome.
Example: EDX.txt upload to samples with distinct chemical system results in different compositions outcome.
=> Show EDX Demo!

## Slide 28: Publications in RDMS
https://inf.mdi.ruhr-uni-bochum.de/rubric/demo_publications
Two types (based on Reference table):
Store publications / presentations / reports in RDMS:
Alternative types to conclude your findings:
PowerPoint Presentation Slides
Report

## Slide 29: Reports: Projects contribution
https://crc1625.mdi.ruhr-uni-bochum.de/report/objectsbymonth?project=A01
https://crc1625.mdi.ruhr-uni-bochum.de/report/projectsstatistics
https://crc1625.mdi.ruhr-uni-bochum.de/report/projectsstatistics?excludeTypes=8
New reports:
Objects by month
Project statistics
What other metrics could help?

## Slide 30: Data Contributions: Establishing KPI == Defining of clear goals
KPI – Key Performance Indicator
What needs to be uploaded?
Upload Data at all stages:
  Experiments plans
  Raw Data
  Processed data
  Reports/Presentations
What data contribution is good enough?
For every project define expected data contributions in RDMS (with numbers):
  How many chemical systems should be explored?
  How many samples should be synthesized?
  How many characterizations should be done?
  Other meaningful metrics (PIs need to define these explicitly!) => INF dashboard
How do you achieve data quality?
Object Type Design (type must contain metrics that allow comparing objects of the type)
  All documents should generate a fingerprint – set of properties, summarizing the data => Findable
  Ideally: no values should be put as text/description

## Slide 31: Attention: Mess up with users
https://crc1625.mdi.ruhr-uni-bochum.de/object/au-cu-pt-109560
https://crc1625.mdi.ruhr-uni-bochum.de/identitymanager/home/users
  Double users!!!
  A02
  A04

## Slide 32: Attention: What are your data?
  A Bad Example of “table” Data for XPS (in CSV format)
  Who could explain it without contacting the author???
https://crc1625.mdi.ruhr-uni-bochum.de/object/ir-pd-pt-rh-ru-121870
https://crc1625.mdi.ruhr-uni-bochum.de/object/xps_10811_10_points-123069

## Slide 33: Improvements Summary
RDMS Core Improvements:
Enhanced templates:
  required properties
  properties-based validation
  properties forms on object creation / file upload
  properties with a controlled drop-down list
New Access Level: ProtectedNDA
Search results improvement (enrich with properties)
SQL / read only API
Advanced object linking: “link type” object to characterize edge in the graph
UDT Web Service Template in C# and Python
Documentation

## Slide 34: Documentation
https://crc1625.mdi.ruhr-uni-bochum.de/home/doc
The link is in the footer on every page:
Documentation content:
User manual
  Many thanks to: Irina Roslyakova, Felix Thelen, Alan Savan, Tobias Piotrowiak, Jill Fortmann, Ellen Suhr, Sabrina Baha, Florian Lourens, Valerie Strotkötter, Rico Zehl, Patrick Marx, Aurelija Mockute, Elaheh Akbarnejad, Sigurd Thienhaus
Presentations, videos
Database structure description (tables and views)
User-defined type (UDT) system:
  Object type configuration
  UDT support API (validation, data extraction, visualization)
  UDT: supported formats (EDX, Resistance, Thickness)
System settings
Tenant settings
API
Source code

## Slide 35: Future plans
Core improvements:
  Integrated dataset generation for a sample / group of samples
  Data pagination / lazy load (performance)
  Data write API (direct connection for external devices to RDMS)
User data formats integration (XRD (ICSD / Pearsons integration), SDC, SECCM)…
Integration with Jupyter Hub (data processing scripts / calculations / ML)
Integration with NFDI (NOMAD by FAIRmat)
External workflow support agent (notifications, TO DO lists, Slack integration)
… your wishes - feel free to suggest

## Slide 36: Contributions are welcome

## Slide 37: New Data Types & Formats Integration in RDMS
Motivation: add more validators/data extractors to enrich materials properties description.
https://crc1625.mdi.ruhr-uni-bochum.de/home/doc
PDF
TXT
CSV
Excel
Can be done in any programming language (Python/C# templates are available)

## Slide 38: Data acquisition API: dashboards & datasets
https://crc1625.mdi.ruhr-uni-bochum.de/home/doc
POST /vroapi/v1/execute
Executes SQL statement and returns dataset (in JSON)
The RDMS exposes all data as read-only views
and downloadable documents
API user can introduce any queries over views
GET /vroapi/v1/download
Downloads document by specified identifier (ObjectId)
Database schema documentation:
https://crc1625.mdi.ruhr-uni-bochum.de/home/doc

## Slide 39: Core RDMS Contributions: Pull Requests, etc
https://gitlab.ruhr-uni-bochum.de
Everybody’s welcome!
Feel free to contribute to open source!
Core INF project:
https://gitlab.ruhr-uni-bochum.de/vic/infproject
Shared projects: 1) Administration User Interface (Identity Manager UI):
https://gitlab.ruhr-uni-bochum.de/vic/identitymanagerui
2) Web Application General Library (WebUtilsLib): https://gitlab.ruhr-uni-bochum.de/vic/webutilslib

## Slide 40: RDMS Free Playground
Playground to test RDMS (multiple tenants with shared users list):
https://inf.mdi.ruhr-uni-bochum.de/
Login and Password (User role): User1@user.org Login and Password (PowerUser role): PowerUser1@user.org Login and Password (Administrator role): Admin1@user.org
https://demo.mdi.ruhr-uni-bochum.de/
https://inf.mdi.ruhr-uni-bochum.de/
  https://inf.mdi.ruhr-uni-bochum.de/
Notes: https://qr.io/

## Slide 41: Announcement: Second RDMS Hands-on Session
When:
Today at 15:20 (till 16:00)
What (possible topics):
  Questions and Answers Session
  Practical use of RDMS (How do I…)
    Upload data
    Create a template (set-up form / table format)
    Search for data
    Use API to extract the data
    Write my own data validation/extraction service & integrate it with RDMS
  Discussions on Data Management (features, workflows, reports, API, etc…)

## Slide 42: Thanks for your kind attention
Questions & Answers
Victor Dudarev
Victor.Dudarev@rub.de
https://vdudarev.ru

## Slide 43: Research Workflow
EDX – Energy-Dispersive X-ray spectroscopy (to determine composition) XRD – X-Ray Diffraction (to determine crystallographic structure) RDM Image source: Yazdi, M., Politze, M. and Müller, M. (2024) ‘A Novel Approach to Outlining Research Data Management Life Cycle: A Case Study’, Research gate, accessed 15.05.2024
Characterisation: EDX, XRD, Resistance, Bandgap, …
Calculation / Compu-tational Composition
Sample
Treatment:
annealing,
oxidation,
polishing, …
Sample_2
Characterisation: EDX, XRD, Resistance, Bandgap, …
Request for Synthesis
Idea or Plan
Report
and RDMS Object Types Interconnection
Research workflow support in RDMS
Defines characterizations
Provides report on samples & measurements